## Slide 1: BARBADOS WORKSHOP
WATER LEVEL DATUM EXERCISES
SILVIA COSTA
Notes: Se puede agregar una imagen encima. Se recomienda formato panorámico

## Slide 2
Navegamos en un buque con 2 metros de calado, 30 metros de eslora y 7 metros de manga. Ahora mismo, estamos cerca de la costa con una profundidad bajo quilla de 6 metros. Conteste a las siguientes preguntas:
El Mareógrafo me indica que en esos momentos estamos en pleamar y tenemos 3.85 metros de altura de marea. En su reseña, indican que el cero del mareógrafo está 0.75 metros por debajo del Cero Hidrográfico. Cual es la altura de la marea sobre el cero hidrográfico?
¿Qué profundidad debería marcar la carta náutica?
Si la diferencia entre el CH y el Nivel Medio del Mar es de 1.5 metros: cual es la profundidad sobre el Nivel Medio del Mar?
Nos han comunicado, que el Cero Hidrográfico empleado en la reseña es erróneo, y el verdadero se encuentra a 0.25 metros por debajo del descrito en la reseña. ¿Cuál es la profundidad sobre el nuevo cero hidrográfico?
Como confirmación, nos dirigimos al anuario, que indica que la pleamar en la que nos encontramos está a 3.40 metros. Sobre que Cero Hidrográfico está proporcionando el dato?
Dibuja siempre el gráfico.
We are navigating a vessel with a draft of 2 meters, a length overall of 30 meters, and a beam of 7 meters. Currently, we are near the coast with an under-keel depth of 6 meters. Please answer the following questions:
The tide gauge indicates that we are at high tide with a tidal height of 3.85 meters. According to your report, the tide gauge zero is 0.75 meters below the nautical chart datum. What is the tidal height relative to the nautical chart?
What depth should the nautical chart display?
If the difference between the nautical chart and the Mean Sea Level is 1.5 meters, what is the depth relative to Mean Sea Level?
It has been communicated to us that the Chart Datum used in the report is incorrect, and the actual datum lies 0.25 meters below the one described in the report. What is the depth relative to the new nautical chart datum?
For confirmation, we consult the tide table, which indicates that the high tide we are experiencing is at 3.40 meters. Relative to which Nautical Chart Datum is this measurement provided?
Always include a diagram.

## Slide 3
Estoy en un muelle midiendo la distancia del “cantil del muelle al nivel del agua”, con las siguientes anotaciones:
Que se produce en este tiempo: ¿pleamar o bajamar?
Si el vértice situado en el cantil del muelle tiene una altura ortométrica de 3 metros, ¿cuáles son las alturas de marea sobre el cero hidrográfico? Teniendo en cuenta que el cero hidrográfico se encuentra 2 metros bajo el NMM.
Si más tarde, nos indican que el vértice mide 3.25 m, tendríamos más o menos altura de marea?
Pero al llegar a la oficina, comprobamos la altura del vértice y tiene 50 cm menos que la altura inicial, ¿qué altura de marea tendríamos?
Al cabo del tiempo, voy con mi equipo GNSS y realizo una medición de la altura elipsoidal, dando 35.60 metros sobre el elipsoide. Cuál es la altura elipsoidal del CH?
Dibuja siempre el gráfico.
I am on a pier measuring the distance from the "pier edge to the water level," with the following recorded data:
What tide phase is occurring during this period: high tide or low tide?
If the benchmark located at the pier edge has an orthometric height of 3 meters, what are the tidal heights relative to the hydrographic zero? Considering that the hydrographic zero is 2 meters below the Mean Sea Level (MSL).
If later we are informed that the benchmark measures 3.25 m, would the tidal height be higher or lower?
Upon arriving at the office, we verify that the benchmark height is 50 cm less than the initial height; what would be the tidal height in this case?
After some time, using my GNSS equipment, I perform an ellipsoidal height measurement, obtaining 35.60 meters above the ellipsoid. What is the ellipsoidal height of the hydrographic zero?
Always include a graph.
10:00 – 2.5 m 10:45 – 3.2 m 11:30 – 3.3 m
10:15 – 2.75 m 11:00 – 3.3 m 11: 45 – 3.2 m
10:30 – 3 m 11:15 – 3.35 m 12:00 – 3 m

## Slide 4
Estoy en un barco hidrográfico, cuyo calado es de 5 m. donde están instalado un GPS de medición RTK, junto con una ecosonda multihaz y mide en su haz central 20 metros de profundidad.
La medida del mareógrafo es de 3 metros de altura de marea. Distando el cero hidrográfico -0.5 m del cero del mareógrafo y -2 m del NMM. ¿Cuál es la profundidad que debería aparecer en la carta náutica? ¿Cuál es la profundidad que debería aparecer en un trabajo referido a la referencia altimétrica nacional?
El GPS RTK tiene un offset vertical con respecto la línea de flotación de 5 metros. Proporciona una altura de 30.50 metros sobre el elipsoide WGS84. Si la ondulación del geoide es de 24 m, cual es la marea medida a partir del dato del GPS RTK sobre el NMM? Y sobre el CH?
¿Cuál es la marea sobre el cero hidrográfico si el valor entre el elipsoide y el cero hidrográfico en ese punto es de 22 m?
Dibuja siempre el gráfico.
I am on a hydrographic vessel with a draft of 5 meters, equipped with an RTK GPS and a multibeam echosounder, which measures a depth of 20 meters at its central beam.
The tide gauge reading is 3 meters of tidal height. The hydrographic zero is located -0.5 meters relative to the tide gauge zero and -2 meters relative to Mean Sea Level (MSL). What depth should be displayed on the nautical chart? What depth should be reported in a survey referenced to the national vertical datum?
The RTK GPS has a vertical offset of 5 meters relative to the waterline. It provides an elevation of 30.50 meters above the WGS84 ellipsoid. Given a geoid undulation of 24 meters, what is the tidal height derived from the RTK GPS data relative to MSL? And relative to the hydrographic zero?
What is the tidal height relative to the hydrographic zero if the height of the nautical chart and the ellipsoid at this location is 22 meters?
Always include the diagram.

## Slide 5
Notes: Esta diapositiva no se debe de modificar ya que es la que permite el cierre con el efecto del escudo reduciéndose