## Slide 1: The GLOSS Programme and Data Portals Angela Hibbert Caribbean Training Course Barbados 17th-21st November

## Slide 2: GLOSS and GOOS
The Global Ocean Observing System (GOOS) is a permanent global system for observations, modelling and analysis of marine and ocean variables to support operational ocean services worldwide.
Responsible to the Intergovernmental Oceanographic Commission Assembly
The Global Sea Level Observing System (GLOSS) is a component of GOOS and aims to:
Establish high quality global and regional sea level networks for application to climate, oceanographic and coastal sea level research
Maintain sea level stations around the world for long term climate change and oceanographic sea level monitoring

## Slide 3: The GLOSS Sea Level Community
Notes: Global Navigation Satellite Systems reflectometry

## Slide 5: The PSMSL
Founded in 1933 "For the study of tides and tidal currents, of other movements of the sea surface and of currents of different origins..."
This was about ocean dynamics and land movement, not monitoring sea level rise!
1936 – decided to produce a volume of globally collected monthly and annual sea level with updates every 5 years.
Primary data source for studies of longer term sea level variability including the reports of the Intergovernmental Panel on Climate Change (IPCC)

## Slide 6: The PSMSL Dataset Today
Contains 54000 station years from >2000 different sites in 200 different countries
All data are freely available for use without restriction from www.psmsl.org, which is updated every Wednesday.

## Slide 7: PSMSL Datasets
Where possible, all data for a station are related through time to a consistent set of locally defined benchmarks.
Two main datasets:
  (1) Revised Local Reference (RLR): with datum control
  (2) Metric: no datum control
Notes: See Phil Woodworth’s talk about this on Friday, but essentially, there are a set of fixed points on land (benchmarks) to which the measuring point and observations of the tide gauge instrument can be related. So, if the technology changes through time, the records from the different technologies can be connected to form one continuous record.

## Slide 8: RLR (Datum Controlled) Dataset

## Slide 9: Longer RLR Records
Notes: Historically, there has been a bias in availability of measurements towards the Northern Hemisphere.

## Slide 10: Latest Available Data
Notes: Some gauges have fallen into disrepair (black and white dots), which is the issue we are currently trying to address in the Caribbean e.g. by installing the St Lucia gauge

## Slide 11: Use of PSMSL data
Global Mean Sea Level reconstruction: from IPCC AR6

## Slide 12: Data Explorer www.psmsl.org/data/obtaining/map.html

## Slide 14: Station Metadata (1) www.psmsl.org/data/obtaining/stations/202.php

## Slide 15: Station Metadata (2) www.psmsl.org/data/obtaining/stations/202.php

## Slide 16: Station Metadata (3) www.psmsl.org/data/obtaining/rlr.diagrams/202.php

## Slide 17: Trend Explorer www.psmsl.org/products/trends/

## Slide 18: www.psmsl.org/data/supplying/

## Slide 19: GNSS-IR Data Portal
https://psmsl.org/data/gnssir/
Global archive for sea level data from GNSS-IR
Contains data from almost 400 GNSS stations globally
Some records extend back 15 years

## Slide 20: GNSS-IR Data Portal

## Slide 21: GNSS-IR Data Portal

## Slide 23: University of Hawaii Sea Level Center
GLOSS Fast and Real-Time Centre
Hourly means of sea level
Fast mode data - ‘light’ QC, released with 1-2 months
Research Quality Data Set (RQDS) produced within 1-2 years
Web site: http://uhslc.soest.hawaii.edu/

## Slide 24: Fast Mode Data

## Slide 25: Research Quality Data Set (RQDS)

## Slide 26: Data Explorer

## Slide 27: Data Explorer

## Slide 28: Data Explorer

## Slide 29: Data Explorer

## Slide 30: Data Explorer
Notes: Benchmarks

## Slide 31: Data Explorer
Notes: Benchmarks

## Slide 32: Data Explorer
Notes: Climatology

## Slide 33: IOC SLSMF

## Slide 34: IOC Sea Level Monitoring Station Facility (SLSMF)
IOC Sea Level Monitoring Facility (IOC SLMF)
Hosted at the Flander Marine Institite (VLIZ)
GLOSS Real-Time Data Centre
High Frequency observations
Not quality-controlled
For operational, early warning purposes
Web site: http://www.ioc-sealevelmonitoring.org
Ideal for daily checks on data availability and quality to support tide gauge technicians

## Slide 35: IOC SLSMF
http://www.ioc-sealevelmonitoring.org
IOC Sea Level Monitoring Facility (IOC SLMF)

## Slide 36: IOC SLSMF
http://www.ioc-sealevelmonitoring.org
IOC Sea Level Monitoring Facility (IOC SLMF)

## Slide 37: IOC SLSMF
IOC Sea Level Monitoring Facility (IOC SLMF)
Switch radio button to absolute levels

## Slide 38: IOC SLSMF
IOC Sea Level Monitoring Facility (IOC SLMF)

## Slide 39: IOC SLSMF
IOC Sea Level Monitoring Facility (IOC SLMF)

## Slide 41: BODC
UK’s National Marine Data Centre
International GLOSS data centre for high frequency delayed-mode data

## Slide 42: BODC

## Slide 44: SONEL
Provides high-quality continuous measurements of sea and land levels at the coast from tide gauges and modern geodetic techniques
SONEL serves as the GNSS data assembly centre for the Global Sea Level Observing System (GLOSS), which is developed under the auspices of the IOC/Unesco.
Provides:
Vertical Land Movement Time Series
GNSS Data Archive for GPS @ Tidegauges

## Slide 45: SONEL

## Slide 46: SONEL

## Slide 47: Nevada Geodetic Laboratory

## Slide 48: Nevada Geodetic Laboratory
Not affiliated with any International Body
Process GNSS data from over 23000 sites around the world
By far the biggest provider of position time series and velocities in the world

## Slide 49: Nevada Geodetic Laboratory
Also provide global estimates of vertical land movement at GPS sites and PSMSL gauge locations
https://geodesy.unr.edu/vlm.php